## Slide 1: Matrix Unit Status Update
Shipped: bpu_sa_array, an 8 × 8 int8 systolic array with INT32 sums
Verified: the exhaustive PE test and four array shapes pass with 0 errors
Measured: first area and FPGA-resource numbers for the PE
Next: choose the decode dataflow, then build the blocks around the array
Notes: This week the first piece of the matrix unit landed in RTL: the PE array, the grid that does the multiply-adds. It passes its self-checking testbench, and we have a first cost comparison. The main open question is how decode maps onto it.

## Slide 2: Where the PE array fits
The first matrix-unit block is in RTL: the PE array, which does the math.
SRAM reads
To build
Stage and unpack
To build
PE array
Shipped
Accumulate and stage
To build
SRAM writes
To build
In bpu_sa_array today
Exact int8 × int8 products, INT32 sums
A tile held in the PEs, double-buffered
8 × 8 default: 64 multiply-adds per cycle
Still to build around it
Commands, sequencing, completion and errors
SRAM fetch and write-back; summing across K
INT4 mode, Q8.24 profiles, block scaling
Notes: The slides from 10-03 split the matrix unit into five stages. The PE array is the one we built: the multiply-adds themselves. Everything around it, from commands to SRAM traffic to summing long dot products, is still to build.

## Slide 3: How the systolic array works
A stays in the PEs, B streams down, and partial sums move right.
B[0]
B[1]
B[2]
D
D
D
D = one-cycle delay
0
PE(0,0)
A[0][0]
PE(0,1)
A[0][1]
PE(0,2)
A[0][2]
+
D
D
C[0]
0
PE(1,0)
A[1][0]
PE(1,1)
A[1][1]
PE(1,2)
A[1][2]
+
D
C[1]
0
PE(2,0)
A[2][0]
PE(2,1)
A[2][1]
PE(2,2)
A[2][2]
+
C[2]
1
A stays in the PEs
PE(i,k) holds one number, A[i][k].
2
B flows down, sums flow right
One B column enters per cycle; each row adds A × B to its sum.
3
Skew in, deskew out
B[k] waits k cycles to meet its sum; the edge realigns the rows, so C leaves as whole columns.
Notes: Each PE holds one number of the A tile. Every cycle a new column of B enters at the top and moves down one PE per cycle, while each row's running sum moves right. The sum leaving the right edge of row i is row i of A dotted with that B column. Column k of B is delayed k cycles on the way in so it meets its sum, and the rows are realigned on the way out, so we push whole columns in and get whole columns out.

## Slide 4: Interface and tile switching
Load A a row at a time, stream B a column per cycle, read C a column per cycle.
Port | Dir | Width | Meaning
clk_i, rst_ni | in | 1 | clock; async reset
mode_i, err_mode_o | in/out | 1 | 1 = int4: unsupported
a_valid_i, a_ready_o | in/out | 1 | A-row handshake
a_row_i | in | Cols × 8 | A row; last row first
a_full_o | out | 1 | a full tile is waiting
b_valid_i, b_ready_o | in/out | 1 | B column; always ready
b_col_i | in | Cols × 8 | one column of B
c_valid_o, c_col_o | out | Rows × AccW | one column of C
Timing and tile switching
C leaves Rows + Cols + 1 cycles after its B column (17 on 8 × 8)
No backpressure on C: add a FIFO if the consumer can stall
The next tile loads into shadow registers while this one computes
The first B column after a_full_o switches to it
Notes: A loads one row per transfer, last row first, because rows shift down the array. B is always accepted. C comes out Rows plus Cols plus one cycles later, in order, with no backpressure, so a consumer that can stall needs a FIFO. While one tile computes, the next one loads into shadow registers; the first B column after a_full_o switches tiles, and the switch travels with that column. INT4 mode is reserved and raises err_mode_o.

## Slide 5: Inside one PE
Each PE multiplies int8 × int8 and adds without propagating a carry.
Operands
a from the active or shadow register; b from above
8 partial products
shifted copies of a, one per bit of b
10 rows
the 8 products plus the incoming sum and carry
Carry-save tree
5 levels of 3:2 adders down to 2 rows, registered
Why carry-save
3:2 adders: three rows in, two out, no ripple
Critical path: mux + AND + 5 full adders
Same delay at any accumulator width
One adder per row, at the edge, finishes it
Worked example: a = 3, b = −2
b = 1111 1110; bit 7 is worth −128
Bits 1–6: 6 + 12 + 24 + 48 + 96 + 192 = 378
Bit 7: −(3 × 128) = −384, so the total is −6 ✓
Notes: Inside each PE, the product a times b is written as eight partial products, one per bit of b, the way you multiply by hand in binary. Together with the incoming sum and carry that's ten numbers, and a tree of carry-save adders squeezes them to two without ever propagating a carry. So the PE's delay is the same at any accumulator width; one ordinary adder per row at the array's edge finishes the job.

## Slide 6: Self-checking testbench
Two testers check every output against a reference model.
1
pe_tester: one PE, every pair
All 65,536 int8 × int8 pairs
Random incoming sum and carry on every pair
Both A paths, alternating: shadow (tile switch) and active
Checks the sum, the B and switch pass-through, and the shadow chain
2
sa_tester: whole array vs a model
Random tiles and B columns; 10% at −128 or 127
Random gaps, overlapped loads and tile switches
A reference model predicts each C column
Checks every column, the flags, and that none go missing
Shapes: 8 × 8, 3 × 5, 5 × 2, 1 × 1
Inputs are driven and outputs checked on the falling clock edge, so the testbench never races the design.
Notes: pe_tester runs every int8 pair through one PE with random incoming sums, alternating between the two ways the PE can read A. sa_tester drives whole arrays with random tiles and columns, random gaps and tile switches, and a reference model that predicts every output column. It runs four shapes at once, including the minimum accumulator widths.

## Slide 7: Test results
The exhaustive PE test and all four array shapes pass with zero errors.
65,536
input pairs into one PE, 0 errors
8,761
array output columns, 0 errors
Shape | AccW | Columns | Tile switches | Errors
8 × 8 | 32 | 2,170 | 139 | 0
3 × 5 | 32 | 2,222 | 306 | 0
5 × 2 | 17 (minimum) | 2,194 | 262 | 0
1 × 1 | 16 (minimum) | 2,175 | 1,136 | 0
Run with Verilator 5.053. Not tested yet: reset in the middle of a run, INT4 mode, gate-level netlists.
Notes: Every check passed. The PE saw all 65,536 input pairs. The four array shapes produced almost nine thousand output columns between them, through more than eighteen hundred tile switches, all matching the model, including the two shapes at the minimum accumulator width. Not covered yet: reset in the middle of a run, INT4, and gate-level netlists.

## Slide 8: First cost comparison
Carry-save buys speed with area, and on the FPGA it can't use DSP blocks.
Area per PE, sky130 (µm²)
Chart: 
| Shipped: carry-save | Plain a × b + psum | Plain, Booth multiplier
Area per PE | 9169 | 5892 | 4825
Yosys, open sky130 library, AccW 32: compare ratios, not absolutes.
Logic delay per PE
3.9 ns vs 5.5 ns
Carry-save vs Booth: about 30% shorter, for about 2× the area
FPGA (UltraScale+, the F2 family)
279 LUTs vs 1 DSP
Carry-save vs plain: 1 DSP + 40 LUTs
Notes: We synthesized one PE two ways: the shipped carry-save PE, and a plain psum plus a times b that lets the tool build the multiplier. On sky130 the carry-save PE is about twice the area for about a thirty percent shorter path, which only pays off at a fast clock. On the FPGA the hand-built tree hides the multiply, so it lands in LUTs instead of a DSP block. These are Yosys numbers: trust the ratios, then redo it in Design Compiler and Vivado.

## Slide 9: Next steps
Decide how decode maps onto the array before tuning the PE.
1
Choose the decode dataflow
Batch-1 decode multiplies a matrix by one vector
An A-stationary array keeps at most 1 row in 8 busy there; prefill uses all of it
2
Pick the PE style per target
One parameter, same numerics
Carry-save where DC says it wins; plain multiply-add on the FPGA, so it uses DSPs
3
Wrap the array
Commands, SRAM fetch and write-back, summing across K
INT4 2×2 mode and the Q8.24 serial profiles
4
Measure with the real tools
Design Compiler sweep across clock targets, team library
Vivado on the F2 part for timing at 250 MHz
Notes: The biggest question isn't the PE, it's the dataflow. Decode at batch one multiplies a matrix by a single vector, and an A-stationary array keeps at most one row of PEs busy there; it shines on prefill. Once that's settled: pick the PE style per target, build the blocks around the array, and measure with Design Compiler and Vivado.